## Slide 1: Simplified Trips-on-Project Software presented at the 15th TRB Conference on Planning Applications Atlantic City, NJ May 17, 2015

## Slide 2: Agenda
STOPS and the FTA Capital Grant Investment Program
How STOPS works
How to work STOPS (abbreviated version)
How to work STOPS (detailed version)
Experiences of early STOPS adopters

## Slide 3: 1. STOPS and the FTA Capital Investment Grant program

## Slide 4: Trips-on-Project forecasting
Topics
  FTA motivations
  Options for project sponsors
  Implications for FTA reviews
  Availability of STOPS and tech support
  Plans for upgrades and extensions

## Slide 5: FTA motivations
Streamlining
  Project-evaluation measures
    Mobility  trips on project (total, transit-dependent)
    Environment  change in auto vehicle-miles traveled
    Cost effectiveness  project cost per trip on project
  Travel forecasting
    FTA to provide a simplified method
    Simplified method to be “good enough”
Reductions in level of effort (sponsors and FTA)

## Slide 6: FTA motivations (continued)
Resulting design standards for STOPS
  Focus on the purpose: trips on major-capital projects  sTOPs
    Urban fixed-guideways: BRT, streetcar, LR, CR, HR
  Use readily-available inputs
    Do not require any primary data collection
    Rely on public, standardized data sources where possible
  Keep it simplified for users
    Provide a graphical user interface
    Limit the number of switches, levers, and dials
  Make it reasonably accurate
    Calibrate with data on many existing systems/lines
    Adjust to local conditions
  Operate on Windows-based computer with no additional software requirements

## Slide 7: Options for project sponsors
Project sponsors may prepare forecasts with:
  Regional travel models
  Incremental models
  STOPS
Sponsors may provide to FTA forecasts from:
  Regional travel models only
  Incremental travel models only
  STOPS only
  Any combination of the above
Augmented with “special market” models, as needed
Augmented with “special market” models, as needed

## Slide 8: Implications for FTA reviews
Source of forecast | FTA review of formally submitted forecasts |  |  | 
 | Transit rider survey data | Properties of the travel model | Validation vs. current riders | Plausibility of forecasts
Regional model |  |  |  | 
Incremental model |  |  |  | 
STOPS |  |  |  | 
Substantial scrutiny
Modest scrutiny
Limited scrutiny
Note that these reviews pertain to formally submitted forecasts. They do not reflect any technical assistance that FTA may have provided to sponsors during the development of forecasting methods or forecasts.

## Slide 9: FTA reviews of STOPS-based forecasts – fall 2014
Procedure
  Triage review
    Consistency of STOPS implementation with current recommendations
    Plausibility of predictions of key ridership characteristics and trips on the project
    Decision on detailed review
  Detailed review
    Potential sources of uncertainties
    STOPS rerun(s) to test possible implications of uncertainties
    Decision on further work with the project sponsor

## Slide 10: FTA reviews of STOPS-based forecasts – fall 2014
Outcomes for the class of 2014 (7 proposed projects using STOPS)
  Triage reviews: 7
  Detailed reviews, reruns: 4
  Discussion with sponsor: 3
  Work with sponsor: 2
  Revised final predictions: 3 (one +, one –, and one – –)
Effort
  Two months; FTA staff and contractor
  Deadline imposed by schedule for annual report to congress
  For 2015, timelines for early submittal of ridership-related materials
    Prepared with locally developed forecasting methods
    Prepared with STOPS

## Slide 11: Availability of STOPS and technical support
Download from the FTA website
  http://www.fta.dot.gov/grants/15682_15620.html
  Software and User Guide
  Sample application
  Census data including the 2000 CTPP
Request help (after good-faith local effort)
  FTA – contact information on STOPS page
  Assistance from FTA contractor at FTA discretion

## Slide 12: 2. How STOPS WORKS

## Slide 13: Overview
2.0 How STOPS works
  2.1 An overview
  2.2 Evolution of STOPS
  2.3 Some details of STOPS v1.50
  2.4 Tests against national ridership experience

## Slide 14: 2.1 An overview

## Slide 15: General characteristics
Modified 4 step trip-based model
  Highway impedances and SE inputs from regional models maintained by MPOs
  Transit paths and impedances directly from transit schedules in GTFS format
  Trip generation and distribution replaced by CTPP seed matrix used to develop person trip tables
  Standard nested logit mode choice model
Automatic calibration
  User-specified region-wide unlinked transit trips
  Transit shares by attraction district from CTPP
  Optionally, observed transit boardings by station group

## Slide 16: STOPS components

## Slide 17: Key characteristics
Person trips
  CTPP replaces trip generation and distribution (for ALL trip purposes)
  Focus on transit-candidate person trips
  No special markets
Transit
  GTFS replaces coded abstract transit network
  Schedule-based path-builder replaces traditional path-builders
Highway
  No internal representation of the highway network
  No assignment, loadings, or loaded conditions
One model to describe transit behavior in dozens of metro areas and differences in actual ridership before and after project implementation in some areas

## Slide 18: 2.2 Evolution of stops

## Slide 19: Evolving understanding of realities
Initial vision:
  Single purpose: predict trips on the project
  ARRF with variable access-mode-specific catchment areas
  No applications where transit-ready models already exist
  Small projects in smaller metro areas
  Transparency more important than processing efficiency
  No requirement for commercial software for travel forecasting, GIS

## Slide 20: Evolving understanding of realities
Evolved vision
  Priority FTA support for project-trip forecasts; help with other uses
  ARRF-like approach inadequate to the task of project-level forecasts
  Applications in metro areas with well-developed travel models
  Projects of all sizes in metro areas of all sizes
  Processing efficiency crucial for huge problem sizes
  Still no commercial software, but looking for a GTFS editor

## Slide 21: Learning from early applications
Unintended situations arose requiring additional error detection
NHB components generated too many trips between and within geographically large or separate CBDs
Single departure time (7:30 am) resulted in:
  Volatile results for longer headway services
  Peak service for very long (e.g., commuter rail) trips occurred before assumed departure time
Station-group factoring may have misled forecasts for new stations
Processing too slow and capacity too limited for very large metro areas
Large CTPP zones in some metro areas distorted forecasts, maybe by a lot

## Slide 22: Updating the software
Version 1.01 – official release in September, 2013
Version 1.02 – official release FTA in February, 2014
Version 1.03 – various interim releases throughout 2014
Version 1.50 – official release on May 6, 2015
  New non-home-based components
  Higher limits on number of zones and stations
  Revised path-builder
  Revised coefficients and nesting structure for mode choice model
  Revised national calibration
  Expanded options for local calibration against station-group counts
  Additional output tables consistent with CGI reporting instructions

## Slide 23: Upgrades and extensions
STOPS v2.01 (beta release anticipated winter, 2015-2016)
  Update to CTPP from the American Community Survey
  Portal for special-market trips from external methods
  Options for easier GTFS editing
Steps
  Incremental method based on local rider-survey data
  Several components from STOPS
    GTFS transit representation and schedule-based path-builder
    Growth factoring over time with population/employment projections
    Highway impedances from the regional travel model

## Slide 24: 2.3 some details of stops v1.50

## Slide 25: Details of STOPS v1.50
Components
  Highway components
  Transit network
  Travel demand and adaptations
  Mode choice
  Automatic adjustments
  Special markets

## Slide 26: STOPS components

## Slide 27: Highway components
Highway impedances
  Zone-to-zone from the regional travel model
  Current year (and future years, if needed)
Calculation of change in person-miles of highway travel (PMHT)
  For each year of interest
  PMHT(I,J) = ∑ [highway person-trips(i,j) x highway distance(i,j)
        + auto-access trips(i,j) x auto-access distance(i,s)]
      Where: I, i = production district and zone
      J, j = attraction district and zone
      s = stop used for park-ride or kiss-ride access
      ∑ = sum over all i,j within each I,J
  PHMT change(I,J) = Build PMHT(I,J) minus No-build PMHT(I,J)

## Slide 28: STOPS components

## Slide 29: Transit network
General Transit Feed Specification (GTFS)
  Key attributes
    Current-year data on actual service!
    Vetted by transit agencies (with inputs from AVLs, operators, and riders)!
    No aggregation (headways) into coded networks with uncertain runtimes!
  Download (sometimes public; more often from transit agencies)
  Edits to represent:
    Current-year No-build (if needed)
    Current-year Build (including adjustments to current routes)
    Future-year(s) No-build and Build (if considered)

## Slide 30: Transit network
Designation of stations
  Aggregation of stop-IDs (train platforms, bus bays, directional stops)
  Degree of vertical separation (for inclusion in impedances)
  Flags on new stations (that are part of “the project”)
  Counts (for use in local calibration)
Designation of park-ride lots
  Location (that STOPS links to proximate stops)
  Type (that defines the catchment area)
  Cost (in minutes to represent parking price, shadow price, vertical separation, others)

## Slide 31: Transit network (continued)
STOPS generation of access, egress, and transfer connections
  Access, egress: For each zone centroid and each eligible transit stop
    Walk: airline distance +10% at 3 mph to/from useful stops within 1.0 miles
    KnR: airline distance at 25 mph to any stop within 3.0 miles or a park-ride lot (using the park-ride rules); and
    PnR: airline distance at 25 mph to user-designated park-ride lots within catchment distance specified for the lot (3, 6, 10, or 25 miles depending on the nature of the lot)
  Transfers: For any pair separated by <0.25 airline miles
    Stop-to-stop or PnR lot-to-stop

## Slide 32: Transit path-building in STOPS GTF Path
Paths and impedances
  Two time periods
    AM peak (one of six possible arrival times 8:00 and 9:00 am)
    Midday (one of six possible arrival times between 1:00 and 2:00 pm)
  Three access type
    Walk
    Kiss-Ride
    Park-Ride
  Three path types
    FG only
    Bus only
    FG-bus

## Slide 33: Transit path-building in STOPS GTF Path (continued)
Schedule-based path selection
  Motivated by required arrival time (no more than 5 minutes late)
  No headways; instead:
    Actual individual vehicle trips
    Actual vehicle-arrival times at stops (based on actual running times)
  Generalized cost (in weighted minutes) for selection of best path
    In-vehicle time (weight = 1.0 minute per minute)
    Walk time (weight = 1.1 minutes per minute)
    PnR and KnR time (weight = 1.5 minutes per minute)
    Wait time (weight = 1.0 minutes per minute)
  Wait time
    Transfers:
      Actual waiting time between vehicle-1 arrival and vehicle-2 departure
      Minus any stop-stop walk time (to avoid double-counting those minutes)
    Arrival-time difference: absolute value of desired-minus-actual arrival times
    First wait: none (perfect scheduling of departure)
    Boarding (5.0 minutes each) to account for uncertainties and inconvenience

## Slide 34: Transit path-building in STOPS GTF Path (continued)
Attributes skimmed from each best path
  Origin-zone and destination-zone
  Origin access mode
  Origin access time
  Transfer walk time
  Destination egress (walk) time
  First wait time plus arrival-time difference
  Transfer wait time
  Number of boardings
  In-vehicle time (fixed guideway and bus, separately)
  Indicator of travel on “the project”
  Path details (for up to four transit boardings)
    Boarding and alighting stops
    Mode (GTFS type)
    GTFS trip_id
For
mode choice
For transit trip loading and summaries

## Slide 35: Transit path-building in STOPS GTF Path (continued)
Sample path report

## Slide 36: Transit-trip loading
Immediately after mode choice for each production-attraction pair
  Have: transit trips by
    Auto ownership
    Trip purpose
    Origin access mode
    Path type
  Accumulate: across each transit boarding, stratified by transit-trip characteristics
    Daily total of boardings on each route by origin mode of access
    Daily total of boardings at each station by station mode of access
    Station-station flows for project-related stations

## Slide 37: STOPS components

## Slide 38: Travel demand
Topics
  CTPP
  Demographics
  Adaptations
    HBW
    HBO
    NHB
    Cloning zones
    Growth factoring
  Mode choice
  Reporting

## Slide 39: CTPP (2000, for now)
Workers by:
  Residence location and workplace location, and
  Household auto ownership, and
  Usual main mode to work
User selections to control CTPP data acquisition by STOPS
  Geography: the single type of geography that STOPS will use
    Tracts – good, because tracts are defined everywhere
    Block groups – better, because they are smaller but used only where selected by MPO/Census Bureau
    TAZs – best, because designed for forecasting but used only where selected by MPO
  State(s), up to three
  MPO, if geography is TAZs or block groups

## Slide 40: Demographics
GIS layer that includes:
  MPO’s TAZ boundaries in latitude/longitude coordinates
    Must be consistent for all MPO-sourced files
      Demographics for every year of interest
      Highway time/distance file with current year, three horizon years
    Do not have to be consistent with boundaries of census zones
  For up to five years (2000, current year, three horizon years)
    Population in each TAZ
    Employment in each TAZ

## Slide 41: Sample demographic file

## Slide 42: Adaptations
Why the context demands adaptability
The kinds of adaptations made on the demand-side of STOPS

## Slide 43
Person trips that are transit candidates
Non-work mode shares
CTPP worker flows by i, j, mode
Transit supply by i, j, path type
Transit survey
(in calibration cities)
Existing transit trips using each transit service (and ultimately the project
What we know
What we need
Transit paths
What we must invent
Adaptations (continued)

## Slide 44: Adaptations: Trip rates
Trip rates: purpose-specific trips per CTPP worker(i,j)
  Derived from NCHRP Report 716 (Quick Response #2), 1997
    HBW trips
      Constant trip rate t(a) for each auto-ownership class
      Calibration parameter C for all auto-ownership classes
      Calibrated so that
        Normalized CTPP transit share x [C x t(a) x CTPP workers(a)]
        = linked HBW transit trips in rider-survey datasets
      Where the CTPP transit share is normalized to match:
        User-provided HBW linked trips on transit, or
        User-provided unlinked trips (assuming 40% HBW and 1.4 boards/linked trip)
    HBO and NHB trips
      Computations similar to HBW trips but:
        Scaled to shares of travel by purpose reported in NCHRP 716
        Decayed with increasing distance
      Calibrated with same approach as HBW trips
  Transit.candidate.trips(i,j,purp) = workers(i,j) x trip.rate(purp)

## Slide 45: Adaptations: Trip rates (continued)
Thoughts on CTPP flows representing HBO travel (in the cloud)
  Observations / hypotheses
    HBO is largest fraction of total person trips but not the largest fraction of transit trips
    HBW and HBO transit trips appear to have similar patterns but with shorter HBO trip lengths
    Same economic drivers (work force and employment) produce and attract both kinds of travel
  Implementation within STOPS
    HBO trips start with CTPP JTW flows (like HBW trips)
    HBO-specific trip rates
    HBO trips drop off more quickly with distance than do HBW trips

## Slide 46: Adaptations: Trip rates (continued)
Thoughts on CTPP flows representing NHB travel (in the cloud)
  Observations / hypotheses
    Workers holding jobs in a neighborhood are attracted to economic activities located in places similar to the residents living in that neighborhood
    NHB transit trips have a shorter average trip length than HBW trips
  Implementation in broad strokes within STOPS
    NHB person trip flows from a zone are scaled by
    (total CTPP attractions in zone) / (total CTPP productions in zone)
    NHB-specific trip rates
    NHB trips drop off more quickly with distance than do HBW trips

## Slide 47: Adaptations: Trip rates (continued)
  Sources
    HBW
      NCHRP 716 HBW trip rates
      Adjusted to match on-board survey trips while holding CTPP transit shares
    HBO
      = HBW rate x (4.0) (the ratio of NHTS HBO/HBW fractions of all travel)
      x 0.37 for 0-car households only, to avoid inflating mode choice K’s
    NHB
      = HBW rate x (2.1) (the ratio of NHTS NHB/HBW fractions of all travel)
      x 0.21 for 0-car households only, to avoid inflating mode choice K’s
Trip rates applied to CTPP worker flows
Transit-candidate trips(i,j) per CTPP worker(i,j)
 | 0 car | 1 car | 2+ cars
HBW | 1.32 | 1.44 | 1.56
HBO | 1.78 | 5.20 | 5.60
NHB | 0.54 | 2.79 | 3.00

## Slide 48: Adaptations: Trip rates (continued)
Distance from i to j (miles)
Non-work Decay Multiplier versus Distance
Decay Multiplier
Chart: 
| 2 | 3 | 4.1666666666666661 | 4.583333333333333 | 5 | 5.416666666666667 | 5.833333333333333 | 6.25 | 6.666666666666667 | 7.083333333333333 | 7.5 | 7.9166666666666661 | 8.3333333333333321 | 8.75 | 9.1666666666666661 | 9.5833333333333339 | 10 | 10.416666666666668 | 10.833333333333334 | 11.25 | 11.666666666666666 | 12.083333333333334 | 12.5 | 12.916666666666668 | 13.333333333333334 | 13.750000000000002 | 14.166666666666666 | 14.583333333333334 | 15 | 15.416666666666668 | 15.833333333333332 | 16.25 | 16.666666666666664 | 17.083333333333332 | 17.5 | 17.916666666666668 | 18.333333333333332 | 18.75 | 19.166666666666668 | 19.583333333333332 | 20 | 20.416666666666668 | 20.833333333333336 | 21.25 | 21.666666666666668 | 22.083333333333332 | 22.5 | 22.916666666666664 | 23.333333333333332 | 23.75 | 24.166666666666668 | 24.583333333333332 | 25 | 25.416666666666664 | 25.833333333333336 | 26.25 | 26.666666666666668 | 27.083333333333332 | 27.500000000000004 | 27.916666666666668 | 28.333333333333332 | 28.749999999999996 | 29.166666666666668 | 29.583333333333332 | 30 | 30.416666666666664 | 30.833333333333336 | 31.25 | 31.666666666666664 | 32.083333333333336 | 32.5 | 32.916666666666664 | 33.333333333333329 | 33.75 | 34.166666666666664 | 34.583333333333336 | 35 | 35.416666666666671 | 35.833333333333336 | 36.25 | 36.666666666666664 | 37.083333333333336 | 37.5 | 37.916666666666664 | 38.333333333333336 | 38.75 | 39.166666666666664 | 39.583333333333329 | 40 | 40.416666666666664 | 40.833333333333336 | 41.25
NCHRP 365 target | 4 | 2.3 | 1.2 | 0.91 | 0.6 | 0.61538 | 0.5 | 0.33

## Slide 49: Adaptations: Growth factoring between years
Basic approach within STOPS
  Compute Y2000 home-end and work-end zone trip ends from existing CTPP JTW
  Estimate forecast year zone trip ends based on increase in zone population (home-end) and employment (work-end)
  IPF CTPP to match future trip ends

## Slide 50: Adaptations: Growth factoring between years (continued)
User-selected options for estimating trip-end growth
  District level: Compute district level population and employment growth ratio and apply to all zones in district
  Zone level:
    Compute 2000 CTPP home trip-ends to population ratio
    Apply ratio to forecast year zone population to compute future home trip ends
    Repeat for work trip ends using employment as basis for growth

## Slide 51: Adaptations: Cloning zones for growth factoring
Problems can occur in high-growth areas
  Sparse residential areas in 2000 that are well populated in forecast year
  Sparse employment areas in 2000 have many jobs in forecast year
Solution
  User assigns one or more “clone” zones for each high-growth zone
  STOPS
    Applies trip patterns (e.g., destinations) from clone zones to the high-growth zone
    Factors trip patterns to maintain trip- ends consistent with forecast-year population and employment
Considerations
  Clone zones must be nearby so that its trip patterns are reasonable for the high-growth zone
  Clone zones must (in aggregate) have development types in 2000 similar to expected development in the high-growth zone for horizon year

## Slide 52: Mode choice
Nested logit model
  Discrete choices
    Auto, non-motorized
    Transit (walk, knr, pnr) x (bus only, fixed-guideway only, bus-and-fixed-guideway)
  Segmentation
    Trip purposes: home-based work, home-based other, non-home-based
    Car ownership: 0 car, 1 car, 2+ cars
    Times of day: peak (for HBW trips), mid-day for non-work trips
  Parameters
    Nesting coefficients:
      0.7 for auto/walk
      0.7 for transit access mode choice
      0.7 x fixed guideway “visibility” (0.1 ≤ visibility ≤ 1.0) for path type choice
    Coefficients on travel times and transit number of transfers
    Static constants:
      Auto, by trip purpose and household auto-ownership
      Transit, by trip purpose, access mode, and household auto-ownership
    Path-type constants
    Local-calibration constants for auto, by attraction district and auto-ownership

## Slide 53: Mode choice tree structure
All-mode person trips
Non-transit
Transit
Auto
Walk
Walk
KNR
PNR
FGO
FGB
Bus
FGO
FGB
Bus
FGO
FGB
Bus
φ=0.7
φ=0.7
φ=0.7*Vis
φ=0.7*Vis
φ=0.7*Vis
Key:
Vis=Guideway visibility factor
FGO=Fixed guideway only
FGB=Fixed guideway+bus
Bus= Bus only

## Slide 54: Mode choice (continued)
Coefficients
  In-vehicle minutes: -0.030 (x 0.8 for fixed-guideway time)
  Walk minutes: 1.0 x C(in-vehicle time)
  First-wait minutes: 1.0 x C(in-vehicle time)
  Transfer-wait minutes: 1.0 x C(in-vehicle time)
  Number of transfers: 5 minutes per transfer

## Slide 55: Mode choice (continued)
Adjustments
  Park-ride circuity
  Walk circuity
  Short FG time on FG/bus path
  Very long walk
  PnR/KnR short transit IVTT
  Auto penalty = f(emp density)

## Slide 56: Mode choice: static constants
 | 0 car | 1 car | 2+ cars
HBW | 0.00 | 0.00 | 0.00
HBO | -1.58 | -47.26 | -24.84
NHB | -0.36 | -76.76 | -56.19
K auto
in minutes added to auto utility
 | 0 car | 1 car | 2+ cars
HBW | 93.62 | 60.64 | 69.08
HBO | 89.76 | 69.01 | 55.73
NHB | 74.50 | 55.73 | 73.34
 | 0 car | 1 car | 2+ cars
HBW | 102.20 | 19.56 | 19.09
HBO | 106.88 | 47.69 | 50.77
NHB | 96.61 | 38.93 | 47.46
K kiss-ride
in minutes added to kiss-ride utility
K park-ride
in minutes added to park-ride utility

## Slide 57: Mode choice: path-type constants
 |  | 0 car | 1 car | 2+ cars
Walk | Bus/FG | 0 | 0 | 11.25
 | Bus only | 0 | 15 | 22.5
Kiss-ride | Bus/FG | 0 | 7.5 | 11.25
 | Bus only | 0 | 15 | 22.5
Park-ride | Bus/FG | 22.5 | 22.5 | 22.5
 | Bus only | 22.5 | 22.5 | 22.5
Path-type constants in minutes of in-vehicle time
Added as penalties to transit utility expressions

## Slide 58: Automatic adjustments with local data
Mode choice
  Constants derived from CTPP attraction shares, by autos owned
  Specific to trip attractions in user-defined districts
  Employed conventionally in utility expressions
Total unlinked transit trips
  Single, fine-tuning factor
  System-wide trips for all trip purposes
  Adjusts trips from mode-choice and transit paths to match user-provided target
Boardings by station-group (SG)
  IPF of SG-to-SG flows
  Depending on method, improves agreement with actual SG counts for existing stations

## Slide 59: Special markets
No explicit treatment of special markets
  Students
  Out-of-town visitors
  International border crossings
  Special events (baseball!)
  Airport access trips by air passengers
  Access to other inter-city terminals
  Inter-city travel
Until STOPS v2.0 is available
  Where special market trips are sizable and relevant to the project
    Calibrate STOPS with special market trips removed from calibration counts
    Use local special market procedures to estimate project ridership
    Manually report sum of STOPS and local special market models
  Where special markets are modest or not relevant to the project
    Run STOPS with total ridership used for calibration but review for distortions

## Slide 60: 2.4 Tests against National ridership experience

## Slide 61: National calibration
Approach – single version of STOPS applied to:
  A national collection of transit systems/projects
  With both static (single time point) and dynamic (before/after) cases
  Employing full local data and automated adjustments
  Through many (many!) iterations and model adjustments
    Observations on residuals versus rider-survey data in previous trials
    Hypotheses on behaviors not yet captured
    Revised relationships, new variables, and/or updated parameters
    New application to full set of urban areas
    Repeat until plausible explanation of behavior yields an acceptable fit of the data
  More influence from the dynamic-calibration cases
No case-specific or type-specific factors or rules introduced to match the data

## Slide 62: National calibration (continued)
Evaluation measures
  Static cases
    Linked transit trips by purpose, autos owned, access mode, path type
    Geographic distribution of transit travel patterns
    Unlinked trips by fixed-guideway mode (light rail, commuter rail, etc.)
    Boardings by station group (before station-group adjustments)
  Before-and-after cases
    Change in linked transit trips
    Trips on projects

## Slide 63: National calibration (continued)
Some problems that led to STOPS revisions
  Overestimates for close-in urban commuter rail stations
  Overestimates for underground and elevated stations
  Poorly represented PnR capture areas
  Incorrect transfer rates
  Heavy-handed influence of station-group factors on new stations
  Missing ridership at stations serving universities
  Struggles with NHB trips
  Inappropriateness of conventional parameters for path choice and mode choice in a setting where schedule-based wait times are available from GTFS data

## Slide 64: Calibration data
Metro area | Comm. rail | Heavy rail | Light rail | Streetcar | BRT | Total
Atlanta |  | 1 |  |  |  | 1
Charlotte * |  |  | 1 |  |  | 1
Denver * |  |  | 1 |  |  | 1
Phoenix |  |  | 1 |  |  | 1
San Diego | 1 |  | 2 |  |  | 3
Salt Lake City * | 1 |  | 1 |  | 1 | 3
Subtotal | 2 | 1 | 6 | 0 | 1 | 10
* Indicates survey data on ridership both before and after recent project openings
Systems with rider survey data

## Slide 65: Calibration data
Metro area | Comm. rail | Heavy rail | Light rail | Streetcar | BRT | Total
Chicago | 1 | 1 |  |  |  | 2
Houston |  |  | 1 |  |  | 1
Kansas City |  |  |  |  | 1 | 1
Minneapolis * | 1 |  | 1 |  |  | 2
Nashville * | 1 |  |  |  |  | 1
Norfolk * |  |  | 1 |  |  | 1
Portland * | 1 |  | 1 | 1 |  | 3
San Jose |  |  | 1 |  |  | 1
SE Florida | 1 | 1 |  |  |  | 2
Seattle | 1 |  | 1 | 1 |  | 3
St. Louis |  |  | 1 |  |  | 1
Tacoma |  |  |  | 1 |  | 1
Subtotal | 6 | 2 | 7 | 3 | 1 | 19
Total | 8 | 3 | 13 | 3 | 2 | 29
* Indicates count data on ridership both before and after recent project openings
Systems with count data only

## Slide 66: National calibration: results
Chart: Actual Daily Fixed Guideway/BRT Ridership (Excluding Special Markets)
| 4829 | 15700 | 11670 | 14700 | 2617 | 3261 | 28339 | 2500 | 1676 | 5369 | 714 | 56220 | 26927 | 32554 | 3376 | 5262 | 24548 | 2358 | 27798 | 101735 | 5562 | 9392 | 102303 | 11237 | 25590 | 11814 | 2843 | 14546 | 70814
Before-After | 5844 | 14069 | 13159 | 11205 | 2285 | 3772 | 23194 | 2738 | 2183 | 6600 | 988
Static | 60277 | 29486 | 34114 | 4537 | 4068 | 32629 | 3663 | 25859 | 100374 | 6960 | 12452 | 84025 | 9792 | 30247 | 10259 | 4609 | 18564 | 81107
Model=Actual | 4829 | 15700 | 11670 | 14700 | 2617 | 3261 | 28339 | 2500 | 1676 | 5369 | 714 | 56220 | 26927 | 32554 | 3376 | 5262 | 24548 | 2358 | 27798 | 101735 | 5562 | 9392 | 102303 | 11237 | 25590 | 11814 | 2843 | 14546 | 70814

## Slide 67: Observations from calibration
Details matter
  Effective district and station group definitions
  Accurate count data
  Accounting for special markets
Don’t be misled by the previous slide. Forecasting is still an uncertain business and that uncertainty must be communicated to decision-makers. Uncertainties include:
  The characteristics of the project itself
  Background assumptions for population, employment,
  Differentiation from competing transit systems
  The accuracy of the forecasting tools

## Slide 68: Recap
STOPS is…
  Data-driven adaptation of conventional trip-based model
    Demand from CTPP
    Transit supply from GTFS schedule data
  Calibrated with national information on project ridership
  Adjusted to match local conditions using actual ridership experience
  More than a sketch planning model
STOPS still requires careful attention to detail to generate reasonable forecasts

## Slide 69: 3. How to work STOPS (Abbreviated version)

## Slide 70: Steps to develop STOPS forecasts
Testing and Core Adjustment
Station Group Calibration and Review
Preparation of Forecasts
Making forecast-ready
Implementation

## Slide 71: Implementation
Set geographic context
  Geography type
  Geographic modeling area
Assemble data
  CTPP
  Regional transit schedules
  Transit ridership counts
Prepare other inputs
  Population and employment forecasts
  Highway travel times
  Station file
  District definitions

## Slide 72: Making forecast-ready
Start simple
  Current year demographics
  Existing transit system
  Required input data (CTPP, GTFS, station file, district file, total unlinked trips)
  Count data (existing fixed-guideway stations)
  Station-group calibration approach set to “01-No Group Calibration”
Make adjustments
  Beginning with error correction
  Ending with fine-tuning
    District definitions
    Station groups
    Calibration methodology
    Station penalties

## Slide 73: Preparation of forecasts
Code project service plan
  Edit existing GTFS to represent project
  Engage schedule-writers to use their scheduling software
Represent growth in demographics
  Review change in forecasted population and employment
  Identify places where simple growth factoring unlikely to succeed
  Clone zones where necessary
  Prepare forecast-year files
  Confirm that STOPS properly represents growth in travel demand
Confirm plausibility of forecasted project ridership
  Remember FTA’s message from the past 25 years:
    Use the forecasting results to tell a coherent story about the role of the project in the regional transit and transportation system

## Slide 74: 4. How to work STOPS (Abbreviated version)

## Slide 75: Topics
Steps to develop STOPS forecasts
  Implementation
  Making forecast-ready
  Preparation of forecasts
Output reports and graphics
Uses for STOPS forecasts
  QC of ridership forecast prepared with other method(s)
  Support of request to FTA

## Slide 76: Steps to develop STOPS forecasts
Testing and Core Adjustment
Station Group Calibration and Review
Preparation of Forecasts
Making forecast-ready
Implementation

## Slide 77: Implementation
Geographic scope of the analysis
  Relevance
    Only for mega-regions: scope may be some subset of the region
    For all other metro areas: scope should be the entire region
  Dimensions
    Geographic area
    Extent of the transit system
  Considerations
    Importance of travel markets to the project
    Focus of calibration on markets relevant to the project
    Processing time, file sizes, and (maybe) STOPS capacity
  Representation in STOPS
    Geographic area: flags on individual CTPP zones
    Transit system: inclusion of GTFS files from individual transit providers

## Slide 78: Implementation (continued)
Data
  2000 Census and CTPP files (from the FTA website)
    Boundary files for Census geography in the appropriate state(s)
    CTPP journey-to-work tabulations (selected tables from Parts I, II, and III)
    Boundary files for census blocks
  GTFS file(s)
    Current file for each relevant transit agency
    Publicly available:
      https://code.google.com/p/googletransitdatafeed/wiki/PublicFeeds
      http://www.gtfs-data-exchange.com
    Available only from the agency: make direct request to agency staff
    Not available: ask anyway; most scheduling software have GTFS as option
  Data from rider counts and surveys
    Total boardings on the “included” system (required by FTA)
    Boardings at existing fixed-guideway stations (required by FTA)
    Boardings at bus stops in the corridor (good practice)
    System-wide total linked transit-trips by trip purpose (optional)

## Slide 79: Implementation (continued)
Data (continued)
  Files from the regional travel model
    Zone-level boundary file
      MPO adopted population and employment
      Years: 2000, current, and (if applicable) horizon year(s)
    Zone-to-zone highway impedances
      Peak-period time and distance
      Years: current and (if applicable) horizon year(s)
    Requirements:
      Consistent zone numbers for both files
      Consistent set of 2000, current, and horizon forecasts
        Boundaries
        Definitions of “employment”
        Forecast series/vintage and/or methodology

## Slide 80: Implementation (continued)
Other input files
  Fixed-guideway stations and selected bus stops (manually coded)
    Station name
    Latitude and longitude
    GTFS stop_id
    Station group
    Grade separation
    Boarding count
    Time penalties
  Definitions of districts (manually coded)
    Aggregations of census zones
    Uses within STOPS
      Calibration of attraction-district transit constants in mode choice
      For growth factoring CTPP flows with population & employment changes
      For reporting of the forecasts

## Slide 81: Making forecast-ready
Testing and core adjustments
  Start simple
    Current year demographics
    Existing transit system
    Required input data (CTPP, GTFS, station file, district file, total unlinked trips)
    Count data (existing fixed-guideway stations)
    Station-group calibration approach set to “01-No Group Calibration”
  Make adjustments beginning with error correction and ending with fine-tuning
Station group adjustments and final review

## Slide 82: Testing and core adjustments
CTPP district calibration and total unlinked trips, no station group calibration
If problems with getting unadjusted STOPS estimates to match observed regional unlinked trips or station group boardings, look for:
  Mechanical errors
  Missing attribute information (time, cost, user preferences) that describe components of the transit system
  Special markets not represented in STOPS (and ought not match)
  Problems with “observed” data
Repeat until confident that STOPS understands markets as well as possible before introducing station group boarding calibration

## Slide 83: Testing: assessment of fit to the data
Basic measures – predicted versus actual:
  Total unadjusted system-wide unlinked trips
  Boardings by station-group
  Boardings on individual routes
Advanced measures (if data are available) – predicted vs. actual:
  District-to-district linked trips
  Station-group to station-group unlinked transit trips

## Slide 84: Local calibration: assessment of fit to the data
Total unadjusted system-wide unlinked trips
  Regional calibration factor computed by STOPS
    target unlinked transit trips
    Factor = --------------------------------------
    raw unlinked transit trips
  Goal: modest calibration factor in the range of 0.7 to 1.3
  Factors outside the range
    Not necessarily fatal but need to be investigated and understood
    Most likely cause is transfer rate that is different from assumption of 1.4 assumed by STOPS in calculation of linked trips from system-wide unlinked trips (when the user does not provide information on system-wide linked trips)
    Remedy: specify the number of system-wide linked HBW trips

## Slide 85: Assessment of fit to the data (continued)
Table 2.04 reports results without any station-group calibration
Regional calibration factor is between 0.7 and 1.3

## Slide 86: Assessment of fit to the data (continued)
Boardings by station-group
  Comparisons
    For existing fixed-guideway stations (required by FTA)
    For bus stops in a subarea (good practice)
  Goal is to have station group boardings* differ from goals by 40% or less so that when station group calibration is applied it will fine-tune results rather than make major adjustments
  Focus attention on:
    High-volume station groups
    Station groups that will influence trips-on-project forecasts
  Factors outside of range, minimize risk to project forecasts
    Identify other factors affecting station use and represent with time penalties
    Include project stations and all nearby stations or stops in same group
    Plan on using station group calibration methods 6, 7, or 8
* Remember, at this stage, station-group calibration is set to option 01 - no calibration

## Slide 87: Assessment of fit to the data (continued)
Table 2.04 (continued) reports results without any station-group calibration
Pre-station- calibration group boardings differ from goals by less than 30%

## Slide 88: Assessment of fit to the data (continued)
Boardings on individual routes
  Comparisons
    Table 10.01 – predicted total boardings by route and access mode
    Compare predicted boardings for the existing system against actual boardings
  Goals
    For routes (in some cases, groups of routes) in the project corridor: ±30 %
    For routes elsewhere: correct order of magnitude

## Slide 89: Advanced assessment of fit to the data
With a reliable on-board survey dataset, tabulate:
  District-to-district linked trips by:
    Trip purpose
    Access mode
    Path type
    Autos owned
With reliable data on station-to-station unlinked trips, tabulate:
  Station-group to station-group unlinked trips
Compare against analogous tables from the STOPS report file
  District-to-district: Tables 15.01 through 350.01
  Station-group to station-group: Table 3.01
  Station-to-station: Tables 15.02 through 350.02

## Slide 90: Core adjustments: find and fix mechanical errors
Common mechanical errors
  Incorrect specification of geography type for CTPP data
  Missing or inconsistent zone-level population and employment
  Reliance on incorrect field in shape file to identify zone number
  Specified date not found in provided GTFS file(s)
  Missing stop_id’s in the station file
  Absent park-ride file where park-ride lots exist or will exist
  Coordinates in some files not in latitude-longitude system
  Inconsistent geographic coverage among:
    CTPP flows
    GTFS files
    Total unlinked and linked transit trips
    Boardings at stations and stops
  Changes to input files not captured in subsequent reapplication
  GTFS filenames too long

## Slide 91: Core adjustments: address other problems
Appropriate actions depend on the nature of the problem
  No action
    Problems relatively minor in extent or magnitude
    Calibration discrepancies not likely to affect project ridership
  Broad adjustments
    Refine estimate of region-wide unlinked transit trips
    Add estimate of linked transit trips by purpose
    Refine district definitions for CTPP transit-shares
  Specific adjustments
    Clone zones to improve grasp of growth patterns 2000current
    Refine station-groupings
    Represent additional local conditions

## Slide 92: Core adjustments: address other problems (continued)
Refine estimate of region-wide unlinked transit trips
  In some situations, the correct number of unlinked transit trips may not be apparent
    STOPS application considers only a portion of the metropolitan area
    GTFS provided for a subset of all transit operators
  Remedy: initial run with best first estimate but then evaluate region-wide scaling, station boardings, route boardings to refine unlinked trip estimate to minimize all factoring
Add estimate of linked transit trips by purpose
  When transfer rates substantially different from 1.4, STOPS may need a heavy adjustment factor to match region-wide unlinked trips
  Remedy: Provide linked trip totals so that STOPS does not have to estimate linked trips by purpose

## Slide 93: Core adjustments: address other problems (continued)
Refine district definitions for CTPP transit-shares
  Initial district level calibration may have missed key attraction locations:
    Specific high transit-share locations diluted inside a larger district
    Large, dispersed, low-transit areas co-mingled with denser, more urban, moderate transit share areas
  Remedy: revise district system to reflect:
    Distinct geographic areas with similar urban form
    Areas with particularly high or low existing transit shares
  Avoid creating too many districts
    CTPP transit trip estimates may become too “lumpy” in lower-ridership areas
    Human reviewers unable to grasp tables larger than 20x20

## Slide 94: Core adjustments: address other problems (continued)
Clone zones to improve grasp of growth patterns 2000current
  Zones with large change in population and employment may have changes in trip patterns that are greater than simple growth in trip ends
    Agrarian town suburban bedroom community
    Suburban bedroom community  major employment activity center
    Employment center  mixed-use urban community
  Remedy: clone zones to copy trip patterns from nearby areas that were similar in 2000 to what exists in the forecast year in the rapidly-growing zone

## Slide 95: Core adjustments: address other problems (continued)
Refine station/stop-groupings
  Have station/stop groups represent geographically contiguous areas organized around:
    Existing fixed guideway
      Line (e.g., north commuter rail, west LRT)
      Area type along a line (e.g., CBD, CBD fringe, urban, suburban)
    Other corridors (including corridors with the project)
      Bus stops in project corridor by area type

## Slide 96: Core adjustments: address other problems (continued)
Application of specific calibration adjustments
  Add station/stop penalties to account for:
    Differences in fare policy
    Conditions that make some stations more or less accessible
    Public perceptions of individual operating agencies/services
    Other large patterns in differences between observed and estimated ridership
  Penalties established through hypothesis, trial, and error.
  Hypotheses are essential-- they help define what adjustments are applied to new stations or stops
  Station/stop penalties are a new STOPS capability and guidance is limited until more experience is gained

## Slide 97: Station group adjustments and final review
Select appropriate method(s) for station group calibration factors
  01 – no calibration: STOPS default
  06 – static factors: STOPS computes factors for each i-j pair and uses identical factors for each scenario.
  07 – district path and access type constants (limited magnitude): STOPS computes production and attraction district constants with impact limited to 0.6 to 1.4
  08 – district path and access type constants (full adjustment): STOPS computes production and attraction district constants with impact limited to 0.3 to 2.0
  09 – factors based on boarding and alighting station: full factoring to match existing counts that are applied to no-build and build scenarios based on station groups used in each scenario
Calibration approaches are a new feature of STOPS and best practices are still emerging

## Slide 98: Initial thoughts on calibration approach
Method | Advantages | Disadvantages | Application
01 – no calibration | No station group “hammers” that may distort results | May not match observed station counts well | Early testing, cases where STOPS naturally matches counts, cases where un-factored results are to be analyzed
06 – static calibration | Good match to counts. Distortions are held constant, less likely to cause unpredictable changes in total linked or unlinked trips | Station adjustments not transferred to similar stations on project unless zone already served by same station group | 
07 – district (limited) | Similar to conventional district level calibration, generates system unlinked trips equal to input number, incremental linked and unlinked trips respond properly to changes in service | May not match station group volumes well. District factors calibrated separately for each access mode and path type. Station adjustments not transferred to projects that change access or path type | May be best approach when model adjustments of under 40% are required to match counts and when district station counts include facilities with same access and path type as those envisioned for project
continued

## Slide 99: Initial thoughts on calibration approach (cont’d)
Method | Advantages | Disadvantages | Application
08 – district (full) | Same as Type 7 but may have better match to counts | Same as Type 7 but with better calibration | Similar to 7 but when higher levels of factoring required
09 – full calibration | Good match to counts. Adjustments developed for station groups applied to new stations with same groups. | Factors may lead to illogical shifts in total unlinked or linked transit trips | Cases where project stations are related to existing station counts with little chance of changing station groups.

## Slide 100: Preparation of forecasts
A calibrated model is just the beginning of the forecasting process
  Coding project service plan
  Representing growth in demographics
  Confirming plausibility of forecasted project ridership

## Slide 101: Coding transit alternatives
Create new GTFS folder with alternative:
  Engage schedule-writers to use existing tools to generate new project schedule; or
  Manually edit existing GTFS to represent project

## Slide 102: Coding transit alternatives (continued)
Some thoughts on a productive strategy
  Structure coding changes into groups. Examples
    Changes related to the project
      The project itself
      Direct competitors
      Feeder services
      Intersecting crosstown routes
      Distant parallel services
    Changes to the overall transit system required to represent horizon year background services
      New fixed guideway services previously committed for implementation
      Expansion of bus services to newly developed areas (in vicinity of the project)
      Reconfiguration of service (e.g., grid system of routes to hub-and-spoke)
      Expansion of bus services to newly developed areas (not near project)

## Slide 103: Coding transit alternatives (continued)
Some thoughts on a productive strategy (continued)
  Build each alternative on the appropriate antecedent
  For each scenario, concentrate on coding a GTFS file set with an appropriate level of changes before coding the next scenario
  For new scenario
    Code highest priority change first
    Run STOPS and record changes in project ridership
    Code and run next highest priority changes. Repeat until expected changes in project ridership are small in comparison to the effort required to code the next round of changes
    For final run in each year, no-build and build must be consistent in terms of geographic coverage and service levels
Current Year Existing
Current Year No-Build
Current Build
Horizon Year No-Build
Horizon Year Build
1
2
3
5
4

## Slide 104: Representing demographic growth
Parallel to process used to represent growth from 2000 to today (discussed earlier)
Since growth to the future cannot be observed, extra attention required concerning plausibility of inputs and resulting trip growth in STOPS
This needs to emphasize the need for another look at corridor growth and consideration of extra steps (cloning) that might be necessary to properly represent future travel

## Slide 105: Confirming plausibility
Everything that FTA has said for the last 25 years still pertains to forecasts generated by STOPS
  Use the forecasting results to tell a coherent story about the role of the project in the regional transit and transportation system

## Slide 106: Output reports and graphics
The information required to tell the story of the project comes from STOPS reports and graphical outputs
STOPS generates 1,021 tables (and up to 14 sub-tables for each main table) with each run. The key is finding what you need.
The report begins with an index of all tables that helps the user locate the information being sought

## Slide 107: STOPS table index
…

## Slide 108: Output reports and graphics (continued)
Useful reports that help support the story of the project:
  District population and employment (Table 12.01)
  District-to-district person travel patterns
    Available for each scenario, trip purpose, auto ownership level (“AllMode” in index)
  Transit trip patterns
    Available for each scenario, trip purpose, auto ownership level, access mode, path type (Linked Trips in index)
  Transit volumes
    Station-station unlinked trips available for each scenario, trip purpose, auto ownership level, access mode, path type (Sta-Sta in index)
    Route level ridership (Table 10.01 and 10.02)
  Change in auto mode PMT (Table 8.01)

## Slide 109: Output reports and graphics (continued)
Change in transit service levels
  See GTFPath path report files in skims\ subdirectory
  Provides listing of selected path for each scenario, access mode, path type, and time period for zone-zone pairs where both the origin and destination zone are named in the district file
STOPS can also display selected transit trip table information using linked GIS functions

## Slide 110: Sample graphical output

## Slide 111: Uses of STOPS
QC of ridership forecast prepared with other method(s)
  Comparison of two forecasts can provide more than twice the insights of either forecast separately
  Details matter in the comparison
    Travel markets
    Market shares
    Changes in transit level-of-service caused by the project
  Differences in outcomes should be explored:
    Data sources?
    Coding errors?
    Differences in model response/elasticity?
  Results lead to two useful outcomes:
    Better understanding of the project’s contributions to mobility
    Identification of potential uncertainties and their sources

## Slide 112: Uses of STOPS (continued)
Support of request to FTA for engineering-entry / funding
  All information for New Starts templates is in STOPS outputs
  No additional tabulations are needed to satisfy the reporting requirements in the results report
  Project sponsors provide to FTA a copy of the entire STOPS implementation (inputs and reports)
    Satisfying the reporting requirements
    Allowing FTA to test answers most questions that may arise without having to bug the sponsor about them
  Project sponsor still required to prepare the story of the mobility benefits of the project from the forecasts